## Slide 1: Voice-to-Writing Robot Project

## Slide 2: Voice-to-Writing Robot Project
The idea is to create a robot that can listen to a spoken word and write it on paper. This project will help you learn how robots can understand human voice and control their movements to do real tasks.

## Slide 3: How the System Works
🎙️ Voice Input The microphone connected to the Raspberry Pi captures the spoken word.
🧠 AI Processing (Speech Recognition) The Raspberry Pi uses a Python-based AI model (like Google Speech Recognition or Whisper) to convert speech into text.
🔄 Communication The Raspberry Pi sends the recognized word to the Arduino Uno through serial communication (USB or GPIO TX/RX pins).
✍️ Robotic Movement The Arduino interprets the text as a command and moves the servo motors to write the word on paper.

## Slide 4: Typical Timeline
Phase | Duration | Description
Hardware setup | 2 week | Assemble components and test wiring
AI speech recognition | 2 weeks | Set up Python code on Raspberry Pi
Serial communication | 1 week | Ensure correct data transfer to Arduino
Motor control and writing logic | 2 weeks | Program servo movements
Testing and refinement | 1 week | Fine-tune accuracy and timing
Total | 8 weeks (~2 months) | 

## Slide 5: Team Roles Example
Role | Responsibility
AI Developer | Handles speech recognition and text processing on Raspberry Pi
Arduino Programmer | Develops servo control code
Electronics Engineer | Connects hardware and ensures power stability
Mechanical Designer | Designs or builds the writing mechanism
Project Leader | Coordinates the team and documents progress

## Slide 6: Main Electronic Components
Item | Quantity | Notes
Raspberry Pi 4 (or 3B+) | 1 | For AI and speech recognition
Micro SD Card (32 GB or more) | 1 | For Raspberry Pi OS
USB Microphone | 1 | To capture voice input
Arduino Uno | 1 | To control the robotic arm
USB Cable (Type A to B) | 1 | Connects Arduino to Raspberry Pi
Breadboard | 1 | For circuit prototyping
Jumper Wires (Male-Male, Male-Female) | 1 pack | For connections between components
Power Adapter (5V 3A for Raspberry Pi) | 1 | Required for stable operation

## Slide 7: Mechanical and Robotic Parts
Item | Quantity | Notes
Servo Motors (SG90 or MG996R) | 3–4 | Control X, Y, Z movement
Robotic Arm Frame (Acrylic or Aluminum) | 1 | Can be DIY or purchased ready
Pen Holder Attachment | 1 | To hold a pen for writing
Paper Platform / Writing Surface | 1 | Stable base for writing
Screws, Nuts, and Mounting Tools | Several | To assemble the arm and servos

## Slide 8: Power and Connectivity
Item | Quantity | Notes
Servo Power Supply (5–6V, 2–3A) | 1 | Separate supply for motors
Power Distribution Board (optional) | 1 | For safe power delivery
Switch or Button | 1 | To start/stop the writing process

## Slide 9: Software Tools
Software | Purpose
Raspberry Pi OS | Operating system for the Pi
Python 3 | Programming AI and communication
Arduino IDE | Coding and uploading Arduino sketches
Libraries: SpeechRecognition, PyAudio, pySerial | For voice recognition and serial communication
Servo Library (Arduino) | To control servo motors